## Slide 1: P4 Runtime API Thoughts on batch operations
Andy Fingerhut
Feb 21, 2018

## Slide 2: Upon what do we build batch operations?
PSA requires individual table add, remove, modify operations to be atomic relative to packet processing by the P4 program.
It does not require a PSA device to be able to implement a ‘transaction’ or ‘batch’ atomically.
  Why not? Because this is not an easy problem to solve in general. In my opinion, building up larger changes that appear ‘atomic’ is best done in control software.
  Let the data plane be optimized for what it needs to do quickly (process packets). Don’t require it be, or contain, a transactional database.

## Slide 3: Some definitions
Atomic batch – Every data packet is guaranteed to be processed according to table contents before the batch began, or after the batch completes.
Non-atomic batch – Every data packet is guaranteed to be processed according to table contents as they are between two individual operations of the batch, but there could be hundreds (or more) of packets processed that ‘see’ each of those intermediate states.

## Slide 4: Easy to implement batch operations
Execute them in order as a non-atomic batch
  (a) Stop immediately if one operation fails, ignoring any operations in the batch after that. Return error status and which operation failed.
  (b) Continue with the sequence regardless of which ones might fail. Return error status listing which operations failed.
  (c) Execute them in an arbitrary order, returning error status listing any that failed. (Some PSA implementations might be able to implement this more efficiently if the order they commit to the data plane is different than the controller gave.)
On failure, it is up to the controller to decide what to do next.

## Slide 5: Doing only the easy ones is enough?
A controller can implement interesting things on top of those.
  For the easy batch operation modes, the batches are really just a mechanism to increase efficiency, avoiding RTT for each individual operation.
Can implement ‘transactions’
  but requires knowledge of the P4 program behavior to do it correctly.
  Details upon request – no slides for that yet.
  I think it is probably a research problem to implement transactions for an arbitrary set of operations, and an arbitrary P4 program, and not limit yourself to ½ of the table entries (see later slide for ½ table entry limit approach).
  Control plane code writers do it for _particular_ P4 programs frequently, though, with common ‘patterns’ existing for how, in any particular case.

## Slide 6: Some properties of hash tables
Why important?
  A common efficient technique to implement tables with exact match keys.
  Hardware implementations all have fixed maximum size at ’pipeline config’ time, and examine at most a small finite number of hash ‘buckets’ per search.
Whether attempting to add an entry fails or succeeds, depends…
  It is data dependent: not only on how many entries, but the values of those entries
  It is operation order dependent:
    You can take two initially empty hash tables, and use different sequences of add and remove operations to get them into different states, even though both end up with the same collection of entries with the same key values.
    In those states, attempting to add key 57 to one might succeed, but for the other would fail.
    (If you know of a practical hash table implementation that avoids this, I would like to learn of it.)

## Slide 7: Easy-to-implement all-or-none batch
This is a non-atomic batch operation, implementing one variant of all-or-none, that is easy to implement.
But, what are its semantics, and are those semantics useful?
  for op in batch_operation_sequence:
    Try op
    if op fails:
      goto ROLLBACK
  return success
  ROLLBACK:
  Let rev_op_sequence start with the last successfully applied op, then continue in the reverse order of batch_operation_sequence;
  for op in rev_op_sequence:
    Try “opposite of op” (i.e. if op is add, do the corresponding remove. If op is remove, do corresponding add)
    if op fails:
      goto ROLLBACK_FAILURE
  return failure; (this kind of failure means everything was successfully undone)
  ROLLBACK_FAILURE:
  // You may think this is impossible, but think about undoing removes on a hash table. Are they guaranteed to be undone?
  // Does a controller want to use an operation like this?
  // It will be responsible for dealing with the data plane in the resulting state where the batch is partially applied.

## Slide 8: Harder-to-implement all-or-none batch
This is also a non-atomic batch operation
It guarantees avoiding the ROLLBACK_FAILURE case on the previous slide, and also can guarantee that it will not touch the data plane state at all unless every operation will succeed.
It is may not look like it, but it is significantly more work to implement than the easy batch ops. E.g. note that if you are doing statistics collection as a background task, you need to either suspend those, or make sure that they are using software state that matches the current hardware state, not the in-memory state that you are building up in memory before executing the writes or failing.
  Make a snapshot of current contents of all tables (e.g. a complete copy, or use persistent data structures to avoid needing to make a complete copy)
  Put code in a mode where all places we would normally write to hardware, we will not write to hardware, but instead record the operation in an in-memory queue.
  for op in batch_operation_sequence:
    Try op
    if op fails:
      goto FAIL
  Execute all writes in the in-memory queue that were recorded
  ”Forget” original in-memory state of the tables, making them match the new hardware state
  goto CLEANUP
  FAIL:
  Discard in-memory queue of hardware writes, without executing any of them
  Restore in-memory data structures tracking table contents to the snapshot made above
  CLEANUP:
  Put code back in mode where hardware writes go through normally

## Slide 9: Atomic batch, limiting to ½ table capacity
This is a general technique to make an arbitrary batch operations atomic relative to packet processing
  If you are willing to limit yourself to half of the data plane’s table capacity
  And there are caveats regarding stateful data plane constructs like counters, meters, and registers.
Near beginning of data plane pipeline, assign each packet a ”color”, initially red.
  All table lookups include the packet color bit as part of the search key, and all table entries do exact match on the color bit.
To implement an atomic batch:
  copy all table entries with color red to another entry in the same table with color blue (this is the step that limits this technique to half of your table capacity)
  Do all batch operations with color blue. These do not affect packet processing yet because all packets flowing through still have color red.
  If any operation fails, delete all of the color blue entries and return failure.
  If all operations succeed, change early table that assigns all packets color red, so now they are all assigned color blue. They start using the new blue table entries, ignoring the old red ones.
  After all color red packets still inside the system are finished and have left, the red table entries can be deleted (or more efficiently, updated to match the current blue entries, so we are ready more quickly for the next atomic batch).
Each successful atomic batch operation toggles the color.
This may be useful in many scenarios, but do you want to require all P4 Runtime API implementations to implement this, all of the time, just in case anyone wants to use it? It seems like a bad idea.
Note that with an appropriately written P4 program, a controller could choose to implement this if it wanted to, and it would only need the easy batch operations to do it.