## Slide 1: P4Runtime, and PSA types with target-specific sizes
Andy Fingerhut
March 21, 2018

## Slide 2: Goals
Enable writing a P4_16 source program myp4prog.p4 that does #include “psa.p4” near the top, and can be compiled to multiple target devices
  without requiring changes to myp4prog.p4 for each target.
For port ids, different targets want to customize the size of type PortId_t in the data plane.
  e.g. maybe vendor device X wants a 7-bit wide value in the data plane for PortId_t, but vendor device Y wants a 15-bit wide value.
  Vendor device X does not want to waste 15-7=8 bits to store a PortId_t in the data plane implementation of P4 programs, just because some other vendor device wants to use that many bits.
As far as possible, controller software does not want to know about these differences.
  It does need to somehow discover and restrict itself to using the physical ports that actually exist on each device, but that does not imply that it needs to know about the custom sizes in the data plane mentioned above.
PortId_t is one example type used in these slides, but there are other similar types defined in PSA.
  PSA v1.0 defines 7 types that are expected to be customized by different vendors
  For the complete list, see: https://p4.org/p4-spec/docs/PSA-v1.0.0.html#sec-psa-type-definitions

## Slide 3: Goals (2)
The P4Runtime wants a P4Info file, auto-generated from myp4prog.p4, that tells a controller most or all of what it needs to know to communicate with a target device that has that P4 program installed into it.
  E.g. if a P4_16 program has a table key with a field named my_funky_field that is type bit<17> in it, P4Info should indicate that the field is type bit<17>.
  For cases where the bit width is explicitly given in myp4prog.p4, both the target-specific data plane implementation and P4Info should reflect that, and the controller will thus be aware of that size. This is expected and normal.
  The potentially tricky part is for the values that the data planes want to have target-specific sizes for.
Generate the target-specific compiled versions (i.e. “binary blobs”) of a P4 program from myp4prog.p4 and the psa.p4 #include file.
  Note: It is OK if psa.p4 is mostly the same, but has target-specific customizations in it. Each vendor will ship its customized psa.p4 file with its target-specific compiler.
Generate the P4Info file from myp4prog.p4, too
  Perhaps in the same compilation run as the target-specific binary blob is created, or it could be a separate invocation of the P4 compiler.
  The P4Info file contents should ideally be identical, regardless of the target device. It should be a function only of myp4prog.p4, regardless of any differences that might exist in target-specific psa.p4 files.
Minimize the number of annotations required in the P4 source code in order to achieve these goals.

## Slide 4
If you disagree with any of the goals, then you can stop here. We should first agree on a set of goals.

## Slide 5: One potential approach
Let each vendor create customized psa.p4 files that they ship with their compiler.
  They contain whatever details are needed so that their compiler will generate target-specific binary blobs that customize the bit widths of values with type PortId_t.
  Other than that, the psa.p4 files for different targets are likely to be very similar.
When a P4Info file is generated from myp4prog.p4, every value of type PortId_t should be described as having size 16 bits.
  Note: This value 16 would be common to _all_ PSA implementations. Every P4 compiler that can generate a P4Info file would know about it, somehow.
  If 16 is not big enough, we should pick a number we can all agree on really, really soon. One that will last a long time, e.g. for the expected lifetime of PSA.

## Slide 6: One potential approach (2)
Result:
  Target X binary blobs will use only 7 bits wherever type PortId_t values appear, but target Y binary blobs will use 15 bits wherever that type appears.
  P4Info file will use 16 bits wherever that type appears.

## Slide 7: Restrictions on writing P4 code
I strongly recommend reading all of this section of the PSA spec.
  https://p4.org/p4-spec/docs/PSA-v1.0.0.html#sec-data-plane-vs-control-plane-values
  It is about 1-2 pages long. It won’t take long to read, really.
Recommendation: Never use hard-coded numeric literal values like 0xfff when comparing values of PortId_t (or the other 6 ‘special’ PSA types), or assigning values to them.
  Instead, limit yourself to obtaining their values from action parameters with values installed by the control plane
  PSA v1.0 defines a named constants that are perfectly fine to use for a couple of special ports:
    PSA_PORT_CPU – the port to/from the CPU
    PSA_PORT_RECIRCULATE – the port to send packets to when you want to recirculate them

## Slide 8: Open issues
How to minimize the annotations needed in a P4_16 program myp4prog.p4 to achieve these effects?
  Ideally such annotations could be limited to only the target-specific psa.p4 file, and need not be sprinkled throughout myp4prog.p4.
  The current open source p4c compiler does not enable this.
    I have created this issue for p4c asking how this might be done.
    https://github.com/p4lang/p4c/issues/1157
    If you think this issue is important, put your +1 or comment on that issue, or convince your representative to the P4_16 language working group to beat the drum on it until it is resolved.
What if my myp4prog.p4 tries to add two values of PortId_t?
  Because of the additional PSA property of there being controller <-> data plane translation of numeric values involved, that is likely a non-portable thing to do that will not lead to happiness.
  Should P4 compilers be _required_ to treat such attempts as errors? Maybe that would be nice to have. Beat on that drum, too, if you care strongly enough about it. The PSA section linked on previous slide already says not to do it, but not everyone reads such things, I know.