## Slide 1: P4 Runtime API Thoughts on batch operations
Andy Fingerhut
Feb 21, 2018

## Slide 2: Upon what do we build batch operations?
PSA requires individual table add, remove, modify operations to be atomic relative to packet processing by the P4 program.
It does not require a PSA device to be able to implement a ‘transaction’ or ‘batch’ atomically.
  Why not? Because this is not an easy problem to solve in general. In my opinion, building up larger changes that appear ‘atomic’ is best done in control software.
  Let the data plane be optimized for what it needs to do quickly (process packets). Don’t require it to be, or contain, a transactional database.

## Slide 3: Some definitions
Atomic batch – Every data packet is guaranteed to be processed according to table contents before the batch began, or after the batch completes.
Non-atomic batch – Every data packet is guaranteed to be processed according to table contents as they are between two individual operations of the batch, but there could be hundreds (or more) of packets processed that ‘see’ each of those intermediate states.

## Slide 4: Easy to implement batch operations
Execute them in order as a non-atomic batch
  (a) “in-order-stop-on-first-failure”: Stop immediately if one operation fails, ignoring any operations in the batch after that. Return error status and which operation failed.
  (b) “in-order-continue-on-failure”: Continue with the sequence regardless of which ones fail. Return error status listing which operations failed.
Execute them in an arbitrary order as a non-atomic batch
  Rationale: Some PSA implementations might be able to implement this more efficiently than in-order-continue-on-failure, if the order they commit to the data plane is different than the controller gave.
  (c) “arbitrary-order-continue-on-failure”: Return error status listing any that failed.
  (d) “arbitrary-order-stop-on-first-failure”: If there is a failure, there is no way to predict in advance which subset will be done and which will not. Still potentially useful if the controller knows that this is OK for its use case, and they want to know about failures quickly because they plan to undo the partial effects if a failure occurs.
On failure, it is up to the controller to decide what to do next.

## Slide 5: Doing only the easy ones is enough?
A controller can implement interesting things on top of those.
  For the easy batch operation modes, the batches are really just a mechanism to increase efficiency, avoiding RTT for each individual operation.
Can implement ‘transactions’
  but requires knowledge of the P4 program behavior to do it correctly.
  See “Atomic switch from old ACL to new ACL” slide later for an example.
  I think it is probably a research problem to implement transactions for an arbitrary set of operations, and an arbitrary P4 program, and not limit yourself to ½ of the table entries (see later slide for ½ table entry limit approach).
  Control plane code writers do it for particular P4 programs frequently, though, with common ‘patterns’ existing for how, in any particular case.

## Slide 6: Some properties of multi-way hash tables
Why important?
  A common efficient technique to implement tables with exact match keys.
  Hardware implementations all have fixed maximum size at ’pipeline config’ time, and examine at most a small finite number of hash ‘buckets’ per search.
  By ‘multi-way’ I mean something like D left or 2-way hashing, generalized to N ways. These calculate 2 or more hash functions on the same key, looking up each hash function as an index into a separate sub-table of hash buckets. Significantly higher utilizations can be achieved with these, versus using only 1 way.
Whether attempting to add an entry fails or succeeds, depends…
  It is data dependent: not only on how many entries, but the values of those entries
  It is operation order dependent:
    You can take two initially empty hash tables, and use different sequences of add and remove operations to get them into different states, even though both end up with the same collection of entries with the same key values.
    In those states, attempting to add key 57 to one might succeed, but for the other would fail.
    (If you know of a practical hash table implementation that avoids this, I would like to learn of it.)

## Slide 7: Easy-to-implement “all-or-none” batch
This is a non-atomic batch operation, implementing one variant of all-or-none, that is easy to implement.
But its behavior is not really “all-or-none”. It is all, or none, or any prefix. This is the same set of final resulting states as you can be in when you use the in-order-stop-on-first-failure mode
  for op in batch_operation_sequence:
    try op
    if (op fails) goto ROLLBACK
  return success
  ROLLBACK:
  Let rev_op_sequence start with the last successfully applied op, then continue in the reverse order of batch_operation_sequence;
  for op in rev_op_sequence:
    try “opposite of op” (i.e. if op is add, do the corresponding remove. If op is remove, do corresponding add)
    if (op fails) goto ROLLBACK_FAILURE
  return failure_and_rollback_succeeded; (this kind of failure means everything was successfully undone)
  ROLLBACK_FAILURE:
  // You may think this is impossible, but think about undoing removes on a multi-way hash table.
  // Are they guaranteed to be undone? [ Answer: No, they can fail. ]
  return failure_and_rollback_failed;

## Slide 8: Harder-to-implement all-or-none batch
This is also a non-atomic batch operation
It guarantees avoiding the ROLLBACK_FAILURE case on the previous slide, and also can guarantee that it will not touch the data plane state at all unless every operation will succeed.
It is may not look like it, but it is significantly more work to implement than the easy batch ops. If you are using an SDK, it might not even provide the hooks necessary to do this at all. E.g. note that if you are doing statistics collection as a background task, you need to either suspend those, or make sure that they are using software state that matches the current hardware state, not the in-memory state that you are building up in memory before executing the writes or failing.
  ret_status = SUCCESS;
  Make a snapshot of current contents of all tables (e.g. a complete copy, or use persistent data structures to avoid needing to make a complete copy)
  Put code in a mode where all places we would normally write to hardware, we will not write to hardware, but instead record the operation in an in-memory queue.
  for op in batch_operation_sequence:
    try op
    if (op fails) goto FAIL
  Execute all writes in the in-memory queue that were recorded
  ”Forget” original in-memory state of the tables, making them match the new hardware state
  goto CLEANUP
  FAIL:
  ret_status = FAILURE;
  Discard in-memory queue of hardware writes, without executing any of them
  Restore in-memory data structures tracking table contents to the snapshot made above
  CLEANUP:
  Put code back in mode where hardware writes go through normally
  return ret_status;

## Slide 9: Atomic batch, limiting to ½ table capacity
This is a general technique to make an arbitrary batch operations atomic relative to packet processing
  If you are willing to limit yourself to half of the data plane’s table capacity
  And there are caveats regarding stateful data plane constructs like counters, meters, and registers.
Near beginning of data plane pipeline, assign each packet a ”color”, initially red.
  All table lookups include the packet color bit as part of the search key, and all table entries do exact match on the color bit.
To implement an atomic batch:
  copy all table entries with color red to another entry in the same table with color blue (this is the step that limits this technique to half of your table capacity)
  Do all batch operations with color blue. These do not affect packet processing yet because all packets flowing through still have color red.
  If any operation fails, delete all of the color blue entries and return failure.
  If all operations succeed, change early table that assigns all packets color red, so now they are all assigned color blue. They start using the new blue table entries, ignoring the old red ones.
  After all color red packets still inside the system are finished and have left, the red table entries can be deleted (or more efficiently, updated to match the current blue entries, so we are ready more quickly for the next atomic batch).
Each successful atomic batch operation toggles the color.
This may be useful in many scenarios, but do you want to require all P4 Runtime API implementations to implement this, all of the time, just in case anyone wants to use it? It seems like a bad idea.
Note that with an appropriately written P4 program, a controller could choose to implement this if it wanted to, and it would only need the easy batch operations to do it.

## Slide 10: General pattern
The atomic batch on previous slide is a general ‘atomic pointer flipping’ technique that can be applied to smaller subsets of tables.
  The ‘pointer’ being flipped in previous slide is the blue/red bit, ‘pointing’ at one of two sets of tables.
Fleshed out example starts on next slide.

## Slide 11: Atomic switch from old ACL to new ACL
Scenario:
  User can configure an ACL (Access Control List) that matches on IP source & dest address, IP protocol, and TCP/UDP source & dest port using ternary matching, with each table entry giving either allow or drop action for packet.
    A single ACL is a named, ordered list of ternary matching rules, each with its own independent allow/drop action.
  Configuration can specify for each input port an ACL name that should be applied to all packets arriving from that input port.
  Currently the configuration has all packets arriving on port P filtered according to the ACL named ‘old_acl’.
  Network operator decides they want to change that to ‘new_acl’.
  Desired behavior in data plane:
    Every packet is processed according to ‘old_acl’, or ‘new_acl’, never something else, i.e. never a portion of ‘old_acl’, or a portion of ‘new_acl’.
    If ’new_acl’ doesn’t fit, fail the attempted config change and keep ‘old_acl’ at all times.

## Slide 12: Pointer-flipping for ACL scenario
P4 code:
  Have a table ‘port_to_acl_id’ that has ingress_port as key, resulting in a control-plane chosen metadata field ‘acl_id’.
    Acl_id’s are just a number dynamically allocated by the control plane, with a different acl_id for each ACL name.
  The ternary ACL lookup table ‘acl_lookup’ has key fields for IP SA, DA, protocol, L4 source & dest port, and the acl_id obtained from earlier port_to_acl_id result.

## Slide 13: Pointer-flipping for ACL scenario (2)
On attempted config change of port P to use ‘new_acl’, control plane can do these things:
  In controller, dynamically allocate a new acl_id A, not currently in use in the data plane for any port.
  Add new entries to table ‘acl_lookup’, all with acl_id A.
    Note that these could use a batch operation with an arbitrary order of committing to the data plane. None of them can be matched by any packets.
    On failure, issue another batch operation to remove any subset of the entries that were successfully added, and fail the configuration change. Note: Removes should never fail.
  If all added successfully, modify table ‘port_to_acl_id’ entry for port P so that packets from that port will now get acl_id A.
  Next packet to access table port_to_acl_id, and all after that, will start matching using the new ‘acl_lookup’ entries with acl_id A, not the old set.
  If the old acl_id for port P is not used by any other port, then after a short time (when the last packet that got the old acl_id) has left the system, safe to delete all ‘acl_lookup’ entries that have that old acl_id.

## Slide 14
Note: This technique is very general, but I don’t know how to automate it for an arbitrary P4 program.
  It might not even be possible: a P4 program that did not have a table that mapped ingress_port to acl_id, and used ingress_port instead of acl_id as a key in the ‘acl_lookup’, would not be able to perform this update atomically
    Unless you pause or drop all traffic from port P while changing the acl_lookup entries for that port. Stopping packet processing during updates from the control plane is another general technique, but one that people would often prefer to avoid using.
  When it is possible, I know of no automated way to detect it.
  How do people survive doing these kinds of things? By creating an ad hoc solution for each case that it matters.
  They are all similar, but so are a lot of other kinds of programs that we write in ad hoc fashion following a well known pattern or style.
Not all use cases need atomic batch updates.
  By far the common case for IP route lookups is to do them one at a time, succeeding or failing independently on each one.